## Slide 1
National Workshop on Experience Sharing under SPMRM on 24th June 2019
Preparation of Gram Panchayat
Spatial Development Plan (GPSDP)
National Institute of Rural
Development and Panchayat Raj
Hyderabad
A collaborative study with
School of Planning and Architecture, Bhopal.
Dr. P Kesava Rao
Associate Professor & Head (CGARD)

## Slide 2: Preparation of Gram Panchayat Spatial Development Plan (GPSDP)
Plan proposal for short term (5 years) for zoning and efficient land utilisation in the rural areas and a participatory spatial planning for Gram Panchayat.
  Identification of Spatial Planning parameters in VDP to be created
  Develop a methodology for inclusion of Spatial Planning at Gram Panchayat Level
  Implementation process under the statute of 73rd Ammendent

## Slide 3
Spatial Attributes
Physical features
Socio‐economic data
Land ownership and holding
Social structure
Housing condition
Decision regarding:
1. Land Use/Zoning
Physical Infrastructure
Participatory Planning and Decision Making
2. Housing and Infrastructure
Social Infrastructure
Draft Report – Recommended process flow , data layers, spatial decision and convergence framework
Non Spatial Attributes

## Slide 5: Location of Selected Village
Selected village lies just outside Bhopal Planning Area boundary.
Selected as an example of peri‐urban village.
Need to prioritize such settlements due to proximity to city.

## Slide 6: Selected Village and Surrounding Settlements
Planning Boundary
Municipal Boundary
Study Area Boundary
Villages Study Villages
Roads
Railway Line Airport
Lake
Oil Depot
Educational Institute

## Slide 7: Socio‐Demographic and Socio‐Economic Baseline from Census (Source: Census, 2011)

## Slide 8: Land Classification as per Census (Source: Census, 2011)

## Slide 13: Existing Framework For Village Planning
Government of Madhya Pradesh passed the Panchayat Adhiniyam 1993 which provides Panchayat for villages, Janpad Panchayats for blocks and District Panchayat for district.
Barkheda Salam GP has single Revenue Village and falls under Phanda Janpad Panchayat within Bhopal Zilla Panchayat.
The village lies outside Bhopal Planning Area and as such, the provisions of the Madhya Pradesh Nagar Tatha Gram Nivesh Adhiniyam do not apply to it.
As per Section 7 of the Madhya Pradesh Panchayat Raj Avam Gram Swaraj Adhiniyam, 1993, Gram Sabha has the power to approve all plans including Annual Plans, programmes and projects for social and economic development.

## Slide 14
Act states that the Gram Sabha shall evaluate next ten years approximate fund to be received, and make a ten years' long term plan for village development, with the help of experts and approve the same.
The plan shall be prepared keeping in view the land use plan and requirement of basic amenities of Gram Sabha, on priority basis of long term plan through a yearly plan based on the financial resources to be received per year to the Gram Kosh of a Gram Sabha.
Currently land use plan for villages not prepared under Act.
Planning is restricted to sectoral planning at present in the form of the GPDP (annual).

## Slide 15: Current GPDP of selected village
No spatial linkage in GPDP. Future land use not envisaged.
Development Control Rules not linked.

## Slide 16
Table 1- 2 Observations/modifications suggested in proposed draft RADPFI during the studies conducted for preparation of model village plan |  |  |  | 
Built up | Use Category | Use category proposed | Activities permitted | Activities proposed to be modified/ added
 | Residential | Residenti al and mixed | Residences* | Residential along with minor commercial activity (daily needs shop, atta chakki, milk selling, dhobi, tea stall, handicraft shop etc)
 | Commercial/ Economic |  | Retail shopping Informal Shop Daily market, weekly, informal , regulated and specialised markets Godowns, Storage grounds | Anaj mandi, petrol pumps, poultry farms, motels, dhaba or restaurants, any other specialized market as per local produce can be listed in this category
 | Utilities and Services |  | Bank, ATM, Credit Society, Police thana, Cremation /Burial ground Crematorium, Community Hall,Dharamshala, Public Toilet, Social Welfare Centre | Waste disposal, water supply, baodies, electric substation and other utilities
 | Special Area |  | Temple, Heritage area, Scenic Value Area, Government Restricted Areas | temple should be replaced by ‘place of worship’

## Slide 17
Non- Built Up Area

## Slide 18: LAYER 1: Evolution of the settlement
Evolution during last 15 yrs (recommended) shown clockwise from 2002 till 2017
Private colonies start emerging around 2010 (after edu hub comes up in neighbourhood)
Inhabited area of village grows in response to the external factors

## Slide 19
MAP THE TEMPORAL GROWTH OF THE SETTLEMENT AND ESTABLISH ‘EXTENSIONS’ BEYOND RECOGNIZED ABADI AREA

## Slide 20: LAYER 2: LAND USE AND BUILT USE
Map overall land use
Land use code decided on the basis of agricultural census and conventional land uses in URDPFI/draft RADPFI guidelines
Land use code may be finalized in consultation with PRD Dept. And/or LR authority of states
Water body
Fallow Land
Abadi Area
Agriculture
Forest
Grazing Land
Industrial
New Residential
PSP
Transport
Barkheda Salam Boundary
Updated Roads
Railways

## Slide 21: AREA DISTRIBUTION
Abadi area consists of approximately 7% of the total area of Barkheda Salam.
It is located centrally in the village along the main road.
18% of the agricultural land has been converted into residential area which is owned by private developers and builders.
The rest of the 81% of the land is restricted to agricultural activities.

## Slide 22: MAP OF ABADI LAND USE
Internal Road
Recreational
Public Semi Public
Residential
Converted Residential
Village Boundary
Contour_10m
Land Use

## Slide 23: Map land ownership Analyze land holding pattern
Government
Private
Ownership

## Slide 24: MAP BUILT USE
Commercial
Mixed
PSP
Residential
Utility
Built Use

## Slide 25: LAYER 3: SOCIO DEMOGRAPHIC ASPECTS
Map relation between settlement and caste/community
Harijan Mohalia
Wdi ohalia
Mandir Mohalia
Mina Mohalia
Romalia Mohalia
Goya Mohalia
Colony Mohalia
Caste

## Slide 26: MAP SPATIAL DISTRIBUTION OF HOUSEHOLDS BY CASTE
Not Known
Ahrwal
Atharwada
Beragi
Gailot
Malviya
Maran
Meera
Mewara
Puri
Rathone
Ruheja
Sen
Soni
Tiwari
ViswaKarma
Yadav
Harijan
Lohar
Caste

## Slide 27: LAYER 4: HOUSING QUALITY
Map spatial distribution of houses by type
Kutcha
Pucca
Semi-Pukka
Kutcha and Pucca
Boundary
Building Type

## Slide 28: MAP SPATIAL DISTRIBUTION BY CONDITION
Dilapidated
Good
Livable
Abad Area Boundary
Building Condition

## Slide 29: Map spatial distribution of houses by age
< 10 years
10 – 20 Years
20 – 50 Years
>50 Years
Abad Area Boundary
Building Age

## Slide 30: Map spatial distribution of buildings by height
G
G+1
G+2
G+3
Abad Area Boundary
Building Height

## Slide 31: Map toilet availability
No
Yes
Built Houses
Toilets

## Slide 32: CROPPING PATTERN
Non Agricultural
Double Crop
Multiple Crop
Single Crop

## Slide 33: Layer 5: agriculture
Map cropping intensity
Non Agricultural
Double Crop
Multiple Crop
Single Crop
Cropping Pattern

## Slide 34
Cropping pattern
Irrigation sources
Livestock

## Slide 35: Layer 6:physical infrastructure
Map road network
Barkheda Salam Boundary
Buildings
Railway Line
Connectivity

## Slide 36: Ped shed analysis
Barkheda Salam Boundary
Roads
Buildings
Railway Line
Infrastructure

## Slide 37: Map water related infrastructure
Barkheda Salam Boundary
Well
Water Line
OHT
Hand Pump
Buidings
Infrastructure -water

## Slide 38: Map open dumping spots
Barkheda Salam Boundary
Open Dumping
Dumping Spots

## Slide 39: Map drainage pattern
Barkheda Salam Boundary
Buildings
Drainage
Drainage

## Slide 40: Layer 7: social infrastructure
Location and accessibility of educational facilities
Barkheda Salam Boundary
School
Buildings
Road
0.5Km
1 Km
Infrastructure

## Slide 41: Location and accessibility of health facilities
Barkheda Salam Boundary
Clinic
Buildings
Road
0.5Km
1 Km
Health Facilities

## Slide 42: Location and accessibility of other social infrastructure
Boundary
Ground
Bank
Temple
PanchayatOffice
School
Community
Hall
Buildings
Social Infrastructure

## Slide 43: Table 4-1: Population Projection
S.No | Population in year |  |  |  |  | 
 | Census |  |  | Existing | Projected | 
Year | 1991 | 2001 | 2011 | 2017 | 2021 | 2023
Population | 1208 | 1533 | 2043 | 2349 | 2521 | 3400

## Slide 44: Land allotment
These are government lands which are illegally encroached and villagers have les or no knowledge about the ownership of land. Most of the villages are grown out of the land allotted for Abadi area.
Old Abadi Area
Extended Aabadi Area
Barkheda Salam Boundary
Allotment

## Slide 45: Land use
Construction on these land parcels put to residential purpose should be done within one year of conversion or else automatically that land will be registered under agriculture and agriculture activity shall be resumed.
Land banks should be created to be given to landless labourers on lease for cultivation.
Abadi area has been extended on major roads.
Road network should be improved as per proposed plan to reduce the spread of Abadi area.
Present density of village abadi area is 143 and for proposed population projection in 2021 will be 164. Abadi area can easily absorb density of 175 pph with the existing transport network, hence no need to expand the abadi area. However the development along the village road contiguous to the original abadi area needs to be regularized as per the provisions of the M. P. Land Revenue Code.

## Slide 46
Colonies/ layouts by SDM as per MP LR code and Madhya Pradesh Gram Panchayat (Registration of Coloniser Terms and Conditions) Rules 1999.
Individual plots by Gram Panchayat as per MP Panchayat Raj Avam Gram Swaraj Adhiniyam 1993

## Slide 49
Phase Sector | Phase 1 (2018-19) |  | Phase 2 (2019-20) |  | Phase 3 |  |  | Phase 4 |  | Phase 5 |  | 
 | Location | Funding Source | Location | Funding Source |  | Location | Funding Source | Location | Funding Source | Location | Funding Source | 
Desilting of water channels | From large water body to Railway line (2km) (A) | Sarpanch Nidhi/ MNREGS | Sham-A- khal to Land of Mr. Jagannath (1 km) (B) | Sarpanch Nidhi/ MNREGS |  | Sham-A- khal to Land of Mr Kisan Rathore (1/2 km) (C) | Sarpanch Nidhi/ MNREGS | Lower Drain Towards Railway line (1km) (D) | Sarpanch Nidhi/ MNREGS | water body | Sarpanch Nidhi/ MNREGS | 
Phase wise marking of proposed drainage network plan supported by funding mechanism and converging financial resources through schemes projects and funds |  |  |  |  |  |  |  |  |  |  |  | 
Village Boundary
Waste Stabilization Pond
1 m
Roads
Proposed Drainage

## Slide 50
Roads
Buildings
Dust Bin
Phase 2
Phase 3
Phase 4
Phase 5
Dust Bin
Dust Bin Locality

## Slide 51: A final Proposed Land use plan compiling all proposals is a must to evaluate the distribution of funds and cumulative spatial implications.
Village Boundary
Road
Railway Line
Proposed Residential
Barren Land
Abadi Area
Water Body
Agriculture
New Residential
Grazing Land
Fallow Land
Industrial
PSP
Transport
Land Use Plan

## Slide 52: Information required by planner before preparation of GPSDP
Land ownership
Cropping pattern
Khasra boundaries
Village boundary map
Abadi area boundary
Public infrastructure
Land rates
Flagship rural development programmes of GoI PMAY‐G, SBM‐G, NRLM, NRHM, SSA,
Ownership of road network
Land conversion policies
Funding mechanisms available

## Slide 54
Planning process followed for preparation of this model Gram Panchayat Spatial Development Plan can be followed across the country. The agro climatic variations across the country demands preparation of model plans in each agro climatic zone.

## Slide 57: Discussions……………